## Slide 1
DESIGN REPORT
KIET GROUP OF INSTITUTIONS GHAZIABAD, UTTAR PRADESH - 201206

## Slide 2
ABOUT
The disaster management and surveillance mission defined under NIDAR has been the primary motivation behind our project, AUTODRAG. Our team has systematically designed a dual-UAV solution focused on rapid area scanning, accurate detection and geotagging of survivors, and precise payload delivery under both manual and autonomous operational modes.
Special emphasis has been placed on hotspot identification, object detection and classification using onboard sensing, and reliable coordination between scanning and delivery platforms to ensure mission effectiveness in time-critical disaster scenarios.
Participation in NIDAR provides our team with a unique opportunity to apply theoretical knowledge to a real-world disaster response application, strengthening our understanding of UAV design, autonomy, avionics integration, and system safety. Through this challenge, we aim to demonstrate a robust, scalable, and competition-compliant UAV system capable of supporting emergency response operations.

## Slide 3
BRIEF
Problem Statement
During disaster situations, reaching affected areas quickly and safely becomes very difficult for rescue teams. Ground search operations take time and are often restricted by damaged infrastructure and unsafe terrain. Our main challenge is to scan large areas quickly, identify survivors accurately, and deliver essential supplies on time without putting human lives at risk. Using a single drone for all these tasks can reduce efficiency, so we needed a better and more reliable approach.
Overall Solution
To solve this problem, we designed a two-drone system. We use a scanning drone to survey the disaster area and detect survivors using onboard camera and processing. Once a location is identified, we accurately mark it using RTK-based GPS. Based on this information, we deploy a separate delivery drone that carries and drops the payload at the required location.
Both drones are operated through a single ground control setup, allowing us to monitor missions and intervene when needed. By separating scanning and delivery tasks, we improve accuracy, reduce mission risk, and ensure smoother operations during disaster response.
MEET THE TEAM:
PRIYANSHU GIRI
AUTOMATION
ASHISH
PROPULSION
HARSHIT
AVIONICS
AYUSH
CAD AND ANALYSIS
ANUBHAV
AUTOMATION

## Slide 4
BRIEF
Problem Statement
During disaster situations, reaching affected areas quickly and safely becomes very difficult for rescue teams. Ground search operations take time and are often restricted by damaged infrastructure and unsafe terrain. Our main challenge is to scan large areas quickly, identify survivors accurately, and deliver essential supplies on time without putting human lives at risk. Using a single drone for all these tasks can reduce efficiency, so we needed a better and more reliable approach.
Overall Solution
To solve this problem, we designed a two-drone system. We use a scanning drone to survey the disaster area and detect survivors using onboard camera and processing. Once a location is identified, we accurately mark it using RTK-based GPS. Based on this information, we deploy a separate delivery drone that carries and drops the payload at the required location.
Both drones are operated through a single ground control setup, allowing us to monitor missions and intervene when needed. By separating scanning and delivery tasks, we improve accuracy, reduce mission risk, and ensure smoother operations during disaster response.
MEET THE TEAM:
SAKSHAM AGGARWAL
KUNAL
UJJWAL GUPTA
ADITYA SINGH
AKARSHI SRIVASTAVA

## Slide 5
BRIEF
Problem Statement
During disaster situations, reaching affected areas quickly and safely becomes very difficult for rescue teams. Ground search operations take time and are often restricted by damaged infrastructure and unsafe terrain. Our main challenge is to scan large areas quickly, identify survivors accurately, and deliver essential supplies on time without putting human lives at risk. Using a single drone for all these tasks can reduce efficiency, so we needed a better and more reliable approach.
Overall Solution
To solve this problem, we designed a two-drone system. We use a scanning drone to survey the disaster area and detect survivors using onboard camera and processing. Once a location is identified, we accurately mark it using RTK-based GPS. Based on this information, we deploy a separate delivery drone that carries and drops the payload at the required location.
Both drones are operated through a single ground control setup, allowing us to monitor missions and intervene when needed. By separating scanning and delivery tasks, we improve accuracy, reduce mission risk, and ensure smoother operations during disaster response.

## Slide 6
DRONE DESIGN

## Slide 7
DELIVERY DRONE

## Slide 8
COMPONENTS USED
S. no. | Description
1. | Flight Controller Pixhawk Cube Orange+
2. | Motor Hobbywing X6 Plus 150KV
3. | Propeller 2480
4. | ESC In-built In motor
5. | T10 TX RX
6. | CUAV C-RTK 2 HP GNSS
7. | Flight Computer Raspberry Pi 5 8GB
8. | 25200mAh 2*6S Battery
9. | Servo Motor MG995
10. | Power Distribution Board PDB-200A

## Slide 9
AVIONCS:
S. no. | Components | Name
1 | Flight Controller | Pixhawk Cube 1Orange
2 | ESC (Electronic Speed Controller) | Cyclone 45A ESC
3 | Transmitter | Skydroid T10
4 | Receiver | T10 Reciever
5 | C-RTK2 HP | RTK GPS Module Compass RM3100
6 | Pixhawk Cube | 3x ICM-45686 Accelerometer/Gyroscope Barometers: 2 x MS5611 Magnetometer: BMM150

## Slide 10
MOTOR:
The propulsion system design began with the selection of a motor suitable for a multi-rotor UAV intended for disaster management operations. After evaluating various high-power propulsion options, the Hobbywing X6 Plus 150KV brushless motor was selected for its high torque output, reliability, and efficient performance with large-diameter propellers. The low-KV configuration enables stable lift at lower rotational speeds, improving flight efficiency, endurance, and control, which are essential for precise maneuvering and payload delivery in emergency response missions
ESC
An Electronic Speed Controller (ESC) is a crucial component in our UAV, acting as the link between the flight controller and motors by regulating power delivery to control motor speed, torque, and thrust precisely.
Each motor is paired with a ReadytoSky OPTO 40A ESC, selected for its 40A continuous current rating, optical isolation, and compatibility with our motor-propeller configuration. The ESC ensures smooth throttle response, reduced electrical noise, and reliable performance under high load conditions.
Specification | 
Continuous Current | 40 A
Burst Current | 60A
Weight(g) | 26g
Length (mm) | 68 mm
Width (mm) | 25 mm
Height (mm) | 8.7 mm
Specification | 
Max Thrust | 11.8kg/Axis (46V, Sea Level)
Weight | 790g
Rated Power Input | 700W
Rated Power Output | 580W
Recommended Battery | 12-14S(LiPo)
PROPULSION SYSTEM:

## Slide 11
ESC
An Electronic Speed Controller (ESC) regulates power delivery from the battery to the motor based on commands from the flight controller, enabling precise control of motor speed and thrust. In this design, the ESC is integrated With the Hobbywing X6 Plus motor, eliminating the need for an external unit and reducing wiring complexity. The in-built ESC ensures smooth throttle response, efficient power management, and reliable performance during high-load and payload-carrying operations.
MOTOR:
The propulsion system design began with selecting a motor suitable for our quadrotor UAV. After evaluating multiple options, the Xing2 3110 900KV Brushless Outrunner Motor was chosen for its balanced performance, delivering high torque and efficient thrust with HQProp 8x4x3 propellers. Each motor produces up to 2000g of thrust, enabling a total of 8000g, resulting in a thrust-to-weight ratio of ~3.8:1, ideal for stable lift and agile manoeuvrability.
Specification | 
Motor Dimensions | Φ38.72 X 24.6 mm
Weight (g) | 80 (including wire)
Max RPM (4S) | 15120
Peak Current (4S) | 40 Amps (estimated with 8x4x3 prop on 4S)
Max. Power(4S) | 672 Watts
Recommended Propeller | 8x4x3
Propellers:
Propellers are mechanical devices that convert rotational motion into thrust. In drones, they generate upward lift by spinning and creating airflow, which causes a pressure difference between the top and bottom surfaces.
We have used HQ 8×4×3 propellers for our drone, which provide an optimal balance between thrust and power consumption when paired with our motors.
Propeller | Thrust | Voltage | Current | Power | Efficiency
HQ 8*4*3 | ~2000g(max) | 16.8V (max) | 40A | 672W | ~2.9g/W
Specification | 
PWM Input Signal Level | 3.3V/5V
Throttle Signal Frequency | 50-500Hz
Operating Pulse Width | 1050-1950us (Fixed or cannot be Programmed)
Max. Input Voltage | 61V
Max. Input Current | 80A (Non-hermetic Ambient Temperature 60°C)
BEC | No
PROPULSION SYSTEM:

## Slide 12
PROPELLERS:
Propellers convert motor rotation into thrust by accelerating airflow. MFP 24×8.0 propellers are selected for their large diameter, enabling efficient lift generation at lower RPMs. This improves flight efficiency and stability, making them well-suited for payload-carrying disaster management operations.
ESC
An Electronic Speed Controller (ESC) is a crucial component in our UAV, acting as the link between the flight controller and motors by regulating power delivery to control motor speed, torque, and thrust precisely.
Each motor is paired with a ReadytoSky OPTO 40A ESC, selected for its 40A continuous current rating, optical isolation, and compatibility with our motor-propeller configuration. The ESC ensures smooth throttle response, reduced electrical noise, and reliable performance under high load conditions.
Specification | 
Continuous Current | 40 A
Burst Current | 60A
Weight(g) | 26g
Length (mm) | 68 mm
Width (mm) | 25 mm
Height (mm) | 8.7 mm
PROPULSION SYSTEM:

## Slide 13
UAS SIZING
    Wheelbase
    The wheelbase is the distance between opposite motors and defines the drone's overall size. For our UAV, a ~450 mm wheelbase offers a balanced platform for stable flight and efficient thrust.
    Rotor Arm Length
    The rotor arm length of our UAV is ~190 mm, providing the necessary clearance for optimal propeller size and efficient thrust generation.

## Slide 14
UAS SIZING
    Hub Size
    The drone’s hub size, measured diagonally between motor mounts, is about ~15.5 mm by
    ~20 mm, ensuring secure motor fit and stable flight.
    Landing Gear Dimensions
    For our drone, the Ground Clearence is ~193 mm, Landing Gear Length is ~213 mm
    providing sufficient clearance from the ground.
    Propeller Clearance
    Propeller clearance is the minimum space between propellers and the drone frame or components to prevent obstruction. Our drone has ~45 mm clearance from body and ~121 mm between propellers for safe, efficient operation.

## Slide 15
FINAL DESIGN CAD MODEL
ANGLE VIEW
FRONT VIEW
TOP VIEW
SIDE VIEW

## Slide 16
COMPUTATIONAL ANALYSIS
In the structural analysis, a 60 N thrust force and a 20 N payload are applied to both the frame and the arm.

## Slide 17
TOTAL DEFORMATION:
Total Deformation is the magnitude of the total displacement of a point in all directions, showing how far that point has moved from its original position.
FRAME:
Maximum Deformation: 12.018
Minimum Deformation: 0 m

## Slide 18
TOTAL DEFORMATION:
Total Deformation is the magnitude of the total displacement of a point in all directions, showing how far that point has moved from its original position.
ARMS:
Maximum Deformation: 12.018 mm
Minimum Deformation: 0 mm
The simulation showed very little deformation in the Frame and Arms, which means the design is structurally strong.

## Slide 19
EQUIVQLENT ELASTIC STRAIN:
Equivalent Elastic Strain is the amount of strain energy per unit volume a material stores under elastic deformation, expressed as a single value, typically used for comparing to yield strain limits.
FRAME:
Maximum Elastic Strain: 0.0043213
Minimum Elastic Strain: 0

## Slide 20
EQUIVQLENT ELASTIC STRAIN:
Equivalent Elastic Strain is the amount of strain energy per unit volume a material stores under elastic deformation, expressed as a single value, typically used for comparing to yield strain limits.
ARMS:
Maximum Elastic Strain: 0.0034692
Minimum Elastic Strain: 0
The strain values stayed within safe limits, indicating the material only experienced elastic deformation.

## Slide 21
EQUIVQLENT STRESS:
Equivalent Stress (also known as von Mises stress) is a calculated value that combines the different normal and shear stress components into one value, making it easier to compare against the material's yield strength.
FRAME:
Maximum Elastic Strain: 137.18 MPa
Minimum Elastic Strain: 0

## Slide 22
EQUIVQLENT STRESS:
Equivalent Stress (also known as von Mises stress) is a calculated value that combines the different normal and shear stress components into one value, making it easier to compare against the material's yield strength.
ARMS:
Maximum Elastic Strain: 18.502 MPa
Minimum Elastic Strain: 0
The stress values were all below the yield strength, confirming that the structure is safe under load.

## Slide 23
SCANNING DRONE

## Slide 24
COMPONENTS USED
S. no. | Description
1. | Flight Controller Pixhawk Cube Orange+
2. | Tarot 4008 330KV Motor
3. | 3K Carbon Fiber Propeller 1755
4. | Cyclone 45A ESC
5. | T12 TX RX
6. | CUAV Neo 3
7. | Flight Computer Raspberry Pi 5 4GB
8. | 8400mAh 2*6S Battery
9. | RunCam Phoenix 2 SP V3
10. | Holybro PM06 V2 Power Module
11. | GEPRC MATEN 5.8G 3W VTX PRO

## Slide 25
AVIONCS:
S. no. | Components | Name
1 | Flight Controller | Pixhawk Orange Cube/+
2 | ESC (Electronic Speed Controller) | Cyclone 45A ESC
3 | Transmitter | Skydroid T10
4 | Power Module | Holybro PM06 V2
5 | GPS | CUAV Neo 3
6 | CUAV Neo 3 | GNSS Receiver IST8310 Compass
7 | Pixhawk Orange Cube/+ | 3x ICM-45686 Accelerometer/Gyroscope (BalancedGyro™ Tech) Barometers: MS5611 Magnetometer: ICM42688 IMU, ICM20948 IMU Accel/Gyro: ICM 20649

## Slide 26
MOTOR:
The propulsion system design began with the selection of a motor suitable for a multi-rotor UAV intended for disaster management operations. After evaluating various high-power propulsion options, the Tarot 4008 330KV brushless motor was selected for its high torque output, reliability, and efficient performance with large-diameter propellers. The low-KV configuration enables stable lift at lower rotational speeds, improving flight efficiency, endurance, and control, which are essential for precise manoeuvring and payload delivery in emergency response missions
ESC
An Electronic Speed Controller (ESC) is a crucial component in our UAV, acting as the link between the flight controller and motors by regulating power delivery to control motor speed, torque, and thrust precisely.
Each motor is paired with a ReadytoSky OPTO 40A ESC, selected for its 40A continuous current rating, optical isolation, and compatibility with our motor-propeller configuration. The ESC ensures smooth throttle response, reduced electrical noise, and reliable performance under high load conditions.
Specification | 
Continuous Current | 40 A
Burst Current | 60A
Weight(g) | 26g
Length (mm) | 68 mm
Width (mm) | 25 mm
Height (mm) | 8.7 mm
PROPULSION SYSTEM:
Specification | 
Max Thrust | 3.5kg
Weight | 85g
Maximum current | 30A
Maximum power | 497W
Recommended Battery | 6S(LiPo)

## Slide 27
ESC
The Cyclone 45A BLHeli-S ESC is a high-performance ESC for multirotor drones, featuring a 6-layer, 3-oz gold-plated PCB for better current handling, heat dissipation, and durability. Its optimized layout ensures strong anti-jamming and stable operation. Supporting DShot 150/300/600, along with Damped Light and regenerative braking, it provides smooth throttle response, fast motor deceleration, and low noise, while an integrated RGB LED improves night-flight visibility.
MOTOR:
The propulsion system design began with selecting a motor suitable for our quadrotor UAV. After evaluating multiple options, the Xing2 3110 900KV Brushless Outrunner Motor was chosen for its balanced performance, delivering high torque and efficient thrust with HQProp 8x4x3 propellers. Each motor produces up to 2000g of thrust, enabling a total of 8000g, resulting in a thrust-to-weight ratio of ~3.8:1, ideal for stable lift and agile manoeuvrability.
Specification | 
Motor Dimensions | Φ38.72 X 24.6 mm
Weight (g) | 80 (including wire)
Max RPM (4S) | 15120
Peak Current (4S) | 40 Amps (estimated with 8x4x3 prop on 4S)
Max. Power(4S) | 672 Watts
Recommended Propeller | 8x4x3
Propellers:
Propellers are mechanical devices that convert rotational motion into thrust. In drones, they generate upward lift by spinning and creating airflow, which causes a pressure difference between the top and bottom surfaces.
We have used HQ 8×4×3 propellers for our drone, which provide an optimal balance between thrust and power consumption when paired with our motors.
Propeller | Thrust | Voltage | Current | Power | Efficiency
HQ 8*4*3 | ~2000g(max) | 16.8V (max) | 40A | 672W | ~2.9g/W
PROPULSION SYSTEM:
Specification | 
Output Voltage | Support 2-6S power supply
Supported protocols | dshot 125/300/600
Power Cord lenght | 18AWG 90mm
Working Current | 35A
Signal line length | 150 mm

## Slide 28
Propellers:
The Carbon Fiber 1755 Propeller (17×5.5) is a lightweight, high-strength propeller designed for high-performance drones and UAVs. It delivers strong thrust, high efficiency, and stable flight with reduced vibration and quick throttle response. Its aerodynamically optimized design and easy, quick installation make it ideal for DIY, multirotor, and professional UAV applications.
ESC
An Electronic Speed Controller (ESC) is a crucial component in our UAV, acting as the link between the flight controller and motors by regulating power delivery to control motor speed, torque, and thrust precisely.
Each motor is paired with a ReadytoSky OPTO 40A ESC, selected for its 40A continuous current rating, optical isolation, and compatibility with our motor-propeller configuration. The ESC ensures smooth throttle response, reduced electrical noise, and reliable performance under high load conditions.
Specification | 
Continuous Current | 40 A
Burst Current | 60A
Weight(g) | 26g
Length (mm) | 68 mm
Width (mm) | 25 mm
Height (mm) | 8.7 mm
PROPULSION SYSTEM:

## Slide 29
UAS SIZING
    Wheelbase
    The wheelbase is the distance between opposite motors and defines the drone's overall size. For our UAV, a ~450 mm wheelbase offers a balanced platform for stable flight and efficient thrust.
    Rotor Arm Length
    The rotor arm length of our UAV is ~190 mm, providing the necessary clearance for optimal propeller size and efficient thrust generation.

## Slide 30
UAS SIZING
    Hub Size
    The drone’s hub size, measured diagonally between motor mounts, is about ~15.5 mm by
    ~20 mm, ensuring secure motor fit and stable flight.
    Landing Gear Dimensions
    For our drone, the Ground Clearence is ~193 mm, Landing Gear Length is ~213 mm
    providing sufficient clearance from the ground.
    Propeller Clearance
    Propeller clearance is the minimum space between propellers and the drone frame or components to prevent obstruction. Our drone has ~45 mm clearance from body and ~121 mm between propellers for safe, efficient operation.

## Slide 31
FINAL DESIGN CAD MODEL
ANGLE VIEW
FRONT VIEW
TOP VIEW
SIDE VIEW

## Slide 32
COMPUTATIONAL ANALYSIS
In the structural analysis, a 60 N thrust force and a 20 N payload are applied to both the frame and the arm.

## Slide 33
TOTAL DEFORMATION:
Total Deformation is the magnitude of the total displacement of a point in all directions, showing how far that point has moved from its original position.
FRAME:
Maximum Deformation: 12.018
Minimum Deformation: 0 m

## Slide 34
TOTAL DEFORMATION:
Total Deformation is the magnitude of the total displacement of a point in all directions, showing how far that point has moved from its original position.
ARMS:
Maximum Deformation: 12.018 mm
Minimum Deformation: 0 mm
The simulation showed very little deformation in the Frame and Arms, which means the design is structurally strong.

## Slide 35
EQUIVQLENT ELASTIC STRAIN:
Equivalent Elastic Strain is the amount of strain energy per unit volume a material stores under elastic deformation, expressed as a single value, typically used for comparing to yield strain limits.
FRAME:
Maximum Elastic Strain: 0.0043213
Minimum Elastic Strain: 0

## Slide 36
EQUIVQLENT ELASTIC STRAIN:
Equivalent Elastic Strain is the amount of strain energy per unit volume a material stores under elastic deformation, expressed as a single value, typically used for comparing to yield strain limits.
ARMS:
Maximum Elastic Strain: 0.0034692
Minimum Elastic Strain: 0
The strain values stayed within safe limits, indicating the material only experienced elastic deformation.

## Slide 37
EQUIVQLENT STRESS:
Equivalent Stress (also known as von Mises stress) is a calculated value that combines the different normal and shear stress components into one value, making it easier to compare against the material's yield strength.
FRAME:
Maximum Elastic Strain: 137.18 MPa
Minimum Elastic Strain: 0

## Slide 38
EQUIVQLENT STRESS:
Equivalent Stress (also known as von Mises stress) is a calculated value that combines the different normal and shear stress components into one value, making it easier to compare against the material's yield strength.
ARMS:
Maximum Elastic Strain: 18.502 MPa
Minimum Elastic Strain: 0
The stress values were all below the yield strength, confirming that the structure is safe under load.

## Slide 39
AUTOMATIC DETECTION
& GEOTAGGING

## Slide 40
Geofence coordinates define the operational boundary of the mission and are uploaded to the drone's flight controller via DroneKit and Mission Planner software. This ensures the UAV remains within designated safety perimeters during autonomous missions.
To guarantee complete coverage of the survey area, a grid flight pattern is implemented
RunCam Phoenix 2 SP V3 camera is mounted downward- facing to capture high-resolution images. Images are taken at consistent intervals and stored for offline processing.
Both are fully autonomous using pre-configured flight modes, enabling seamless mission execution.
  Our UAV system integrates a Raspberry Pi 5 as the companion computer. The system leverages DroneKit Python scripts to automate flight operations, and communicates with the Pixhawk flight controller using the MAVLink protocol.
1
2
3
4
Geofence Integration
Grid Path Planning:
Camera and Imaging Setup:
Takeoff and Landing

## Slide 41
AUTONOMY AND DEPLOYEMENT
Mission Planner is used to create autonomous missions for both scanning and delivery drones.
Grid-based waypoints are defined for area scanning, while target-specific waypoints are used for payload delivery.
The planned mission is uploaded to the Pixhawk flight controller, and the drone operates in AUTO mode.
Mission Planner enables real-time monitoring of position, altitude, and mission progress.
Safety features such as mode switching and Return-to-Launch (RTL) ensure safe deployment and recovery.

## Slide 42
AUTOMATIC IDENTIFICATION:
The scanning drone flies autonomously using grid-based waypoints and automatically detects humans using onboard vision processing.
1.
Once a human is detected, the system automatically records the drone’s GPS coordinates (latitude, longitude, altitude, timestamp) and saves the location as a waypoint.
2.
The detected waypoints are automatically uploaded to the cloud and made available to the delivery drone without manual coordinate entry.
3.
The delivery drone retrieves the waypoints, navigates autonomously to each location, releases one payload per waypoint, and returns to launch after completing the mission.
4.

## Slide 43
WAYPOINT EXECUTION PROCESS
EXTRACTING LOCATIONS:
SAVING WAYPOINTS TO CLOUD

## Slide 44
WAYPOINT EXECUTION PROCESS
SENDING DATA TO DELIERY DRONE:
COMPLETING THE MISSION:

## Slide 45
SUBSYSTEM SELECTION

## Slide 46
CONTROL & COMMUNICATION SYSTEM
Subsystem | Delivery Drone | Scanning Drone | Purpose
Transmitter (GCS Input) | Radiomaster T10• 2.4 GHz FHSS• 10 Channels• Long operating time | Skydroid T12• 2.4 GHz• Up to 12 Channels• Integrated GCS display | Manual control, mode switching, safety override
Receiver | Radiomaster Receiver• 2.4 GHz• Telemetry support | Skydroid Receiver• 2.4 GHz• Telemetry support | Receives control commands from GCS
Flight Controller | Pixhawk Cube Orange Plus• Redundant sensors• ArduPilot/PX4 | Pixhawk Cube Orange / +• Redundant sensors• ArduPilot/PX4 | Stabilization, navigation, autonomy
GPS Module | CUAV Here 3+ CAN GNSS• RTK enabled• cm-level accuracy | CUAV Neo 3 GNSS• Multi-constellation• High sensitivity | Positioning, waypoint navigation, RTL
Companion Computer | Raspberry Pi 5 (4/8 GB)• Mission logic• Payload control | Raspberry Pi 5 (8 GB)• Vision processing• Target detection | High-level processing & autonomy
Video System | FPV Cam + VTX (5.8 GHz) | FPV Cam + VTX (5.8 GHz) | Live video feedback to operator
Power Monitoring | Holybro PM06 V2 | Holybro PM06 V2 | Voltage & current sensing
Communication Protocol | MAVLink (internal) | MAVLink (internal) | FC ↔ Companion ↔ GCS communication

## Slide 47
MULTIDRONE OPERATION

## Slide 48
PAYLOAD DROPPING MECHANISM

## Slide 49
PAYLOAD CAD:
ANGLE VIEW
FRONT VIEW
TOP VIEW
SIDE VIEW

## Slide 50
FAILSAFE AND SAFETY
FEATURES

## Slide 51
FAILSAFE AND SAFETY FEATURES
If the radio link between transmitter and receiver is lost, the Pixhawk detects signal failure.
Upon signal loss, the flight controller automatically executes a predefined failsafe action such as Return-to-Launch (RTL) or landing.
The Holybro PM06 V2 power module is connected between the battery and Pixhawk flight controller.
It continuously measures battery voltage and current and sends this data to the Pixhawk.
When voltage drops below the set threshold, the Pixhawk triggers low-battery failsafe such as RTL or auto-land.
Battery Failsafe (Power Module–Based)
Radio Failsafe (Communication Loss)

## Slide 52
THANK YOU
JAI HIND